Un estimador de error para un método sin malla en problemas de potencial de 2D

Beatriz Alonso Santosa, Luis Gavete Corvinosa

a Dpto. de Matemática Aplicada a los Recursos Naturales. Universidad Politécnica de Madrid. beatriz.alonso@upm.es

Resumen

En esta comunicación se presenta un método para estimar los errores local y global en el método de Galekin libre de elementos. Este estimador utiliza la solución proporcionada por el método sin malla anterior y la aproximación de mínimos cuadrado móviles, ya que se calcula  como la diferencia entre dos aproximaciones de los gradientes  obtenidas usando la solución proporcionada por el método de Galerkin libre de elementos y dos radios de influencia diferentes. Este estimador es sencillo y fácil de implementar.

La eficiencia de dicho estimador se demuestra analizando problemas de potencial en dos dimensiones usando disposiciones de puntos regulares e irregulares.

Su implementación permite obtener la norma global de energía así como evaluar errores locales, lo que permitiría realizar el método adaptativo.

Palabras clave: Método sin malla, Galerkin libre de elementos, error a posteriori, problema de potencial

A posterior error estimation for a meshless method applied to 2D potential problem

Beatriz Alonso Santosa, Luis Gavete Corvinosa

a Dpto. de Matemática Aplicada a los Recursos Naturales. Universidad Politécnica de Madrid. beatriz.alonso@upm.es

Abstract

In this paper, an  easy method to estimate the local and global errors in the Element Free Galerkin method, EFG, is proposed utilising the moving least squares approximation, MLS, together with the computed EFG solutions. The error approximation is calculated     as  the difference between two MLS approaches for the gradients that are obtained from the EFG solution uh , using two different radii of influence(rinf). The procedure described in the paper is simple and can be easily implemented.

The performance of the developed approximation of the error is illustrated by analysing different examples for 2-D potential problems using regular and irregular clouds of points. The implemented procedure of error approximation allows the global energy norm error to be estimated and also gives a good evaluation of local errors, so an adaptive method can be implemented.

Palabras clave: Meshless, Element Free Galerkin, a posteriori error , potencial problem